## Slide 1: Digital Design & Computer Arch. Lecture 10a: Instruction Set Architecture
Prof. Onur Mutlu
ETH Zürich
Spring 2020
20 March 2020

## Slide 2: Assignment: Required Lecture Video
Why study computer architecture?
Why is it important?
Future Computing Architectures
Required Assignment
  Watch Prof. Mutlu’s inaugural lecture at ETH and understand it
  https://www.youtube.com/watch?v=kgiZlSOcGFM
Optional Assignment – for 1% extra credit
  Write a 1-page summary of the lecture and email us
    What are your key takeaways?
    What did you learn?
    What did you like or dislike?
    Submit your summary to Moodle – Deadline: March 25

## Slide 3: Extra Assignment: Moore’s Law (I)
Paper review
G.E. Moore. "Cramming more components onto integrated circuits," Electronics magazine, 1965
Optional Assignment – for 1% extra credit
  Write a 1-page review
  Upload PDF file to Moodle – Deadline: April 1
I strongly recommend that you follow my guidelines for (paper) review (see next slide)

## Slide 4: Extra Assignment: Moore’s Law (II)
Guidelines on how to review papers critically
  Guideline slides: pdf ppt
  Video: https://www.youtube.com/watch?v=tOL6FANAJ8c
  Example reviews on “Main Memory Scaling: Challenges and Solution Directions” (link to the paper)
    Review 1
    Review 2
  Example review on “Staged memory scheduling: Achieving high performance and scalability in heterogeneous systems” (link to the paper)
    Review 1

## Slide 5: Agenda for Today & Next Few Lectures
LC-3 and MIPS Instruction Set Architectures
LC-3 and MIPS assembly and programming
Introduction to microarchitecture and single-cycle microarchitecture
Multi-cycle microarchitecture

## Slide 6: Required Readings
This week
  Von Neumann Model, LC-3, and MIPS
    P&P, Chapters 4, 5
    H&H, Chapter 6
    P&P, Appendices A and C (ISA and microarchitecture of LC-3)
    H&H, Appendix B (MIPS instructions)
  Programming
    P&P, Chapter 6
  Recommended: H&H Chapter 5, especially 5.1, 5.2, 5.4, 5.5
Next week
  Introduction to microarchitecture and single-cycle microarchitecture
    H&H, Chapter 7.1-7.3
    P&P, Appendices A and C
  Multi-cycle microarchitecture
    H&H, Chapter 7.4
    P&P, Appendices A and C

## Slide 7: Recall: The Instruction Cycle
  FETCH
  DECODE
  EVALUATE ADDRESS
  FETCH OPERANDS
  EXECUTE
  STORE RESULT

## Slide 8: Instruction Set Architectures

## Slide 9: Recall: The Instruction Set Architecture
The ISA is the interface between what the software commands and what the hardware carries out
The ISA specifies
  The memory organization
    Address space (LC-3: 216, MIPS: 232)
    Addressability (LC-3: 16 bits, MIPS: 32 bits)
    Word- or Byte-addressable
  The register set
    R0 to R7 in LC-3
    32 registers in MIPS
  The instruction set
    Opcodes
    Data types
    Addressing modes
Microarchitecture
ISA
Program
Algorithm
Problem
Circuits
Electrons
Notes: x86-64:
* Memory organization:
- Address space: up to 2^48.
- Addressability: up to 48 bits. The actual length of the address is 64 bits, but bits 48 to 63 are sign extended.
* Register set:
16 GPR, including RBP (stack base pointer) and RSP (stack pointer).
+ floating point, multimedia

## Slide 10: Recall: Opcodes in LC-3

## Slide 11: Recall: Opcodes in LC-3b

## Slide 12: Recall: Funct in MIPS R-Type Instructions (I)
Harris and Harris, Appendix B: MIPS Instructions
Opcode is 0 in MIPS R-Type instructions.
Funct defines the operation

## Slide 13: Recall: Funct in MIPS R-Type Instructions (II)
Harris and Harris, Appendix B: MIPS Instructions
Find the complete list of instructions in the appendix

## Slide 14: Data Types
An ISA supports one or several data types
LC-3 only supports 2’s complement integers
  Negative of a 2’s complement binary value X = NOT(X) + 1
MIPS supports
  2’s complement integers
  Unsigned integers
  Floating point
Again, tradeoffs are involved
  What data types should be supported and what should not be?

## Slide 15: Data Type Tradeoffs
What is the benefit of having more or high-level data types in the ISA?
What is the disadvantage?
Think compiler/programmer vs. microarchitect
Concept of semantic gap
  Data types coupled tightly to the semantic level, or complexity of instructions
Example: Early RISC architectures vs. Intel 432
  Early RISC machines: Only integer data type
  Intel 432: Object data type, capability based machine
  VAX: Complex types, e.g., doubly-linked list
Notes: Semantic level = how close are the instructions to the constructs of the program

## Slide 16: Addressing Modes
An addressing mode is a mechanism for specifying where an operand is located
There five addressing modes in LC-3
  Immediate or literal (constant)
    The operand is in some bits of the instruction
  Register
    The operand is in one of R0 to R7 registers
  Three of them are memory addressing modes
    PC-relative
    Indirect
    Base+offset
In addition, MIPS has pseudo-direct addressing (for j and jal), but does not have indirect addressing

## Slide 17: Operate Instructions

## Slide 18: Operate Instructions
In LC-3, there are three operate instructions
  NOT is a unary operation (one source operand)
    It executes bitwise NOT
  ADD and AND are binary operations (two source operands)
    ADD is 2’s complement addition
    AND is bitwise SR1 & SR2
In MIPS, there are many more
  Most of R-type instructions (they are binary operations)
    E.g., add, and, nor, xor…
  I-type versions (i.e., with one immediate operand) of the R-type operate instructions
  F-type operations, i.e., floating-point operations

## Slide 19: NOT in LC-3
NOT assembly and machine code
NOT R3, R5
LC-3 assembly
Field Values
Machine Code
9
3
5
1 1 1 1 1 1
OP
DR
SR
1 0 0 1
0 1 1
0 0 1
1 1 1 1 1 1
OP
DR
SR
15
12
11
9
8
6
0
5
Register file
SR
DR
From FSM
There is no NOT in MIPS. How is it implemented?

## Slide 20: Operate Instructions
We are already familiar with LC-3’s ADD and AND with register mode (R-type in MIPS)
Now let us see the versions with one literal (i.e., immediate) operand
Subtraction is another necessary operation
  How is it implemented in LC-3 and MIPS?

## Slide 21: Operate Instr. with one Literal in LC-3
ADD and AND
  OP = operation
    E.g., ADD = 0001 (same OP as the register-mode ADD)
      DR ← SR1 + sign-extend(imm5)
    E.g., AND = 0101 (same OP as the register-mode AND)
      DR ← SR1 AND sign-extend(imm5)
  SR1 = source register
  DR = destination register
  imm5 = Literal or immediate (sign-extend to 16 bits)
OP
DR
SR1
1
imm5
4 bits
3 bits
3 bits
5 bits

## Slide 22: ADD with one Literal in LC-3
ADD assembly and machine code
ADD R1, R4, #-2
LC-3 assembly
Field Values
Machine Code
1
1
4
1
-2
OP
DR
SR
imm5
0 0 0 1
0 0 1
1 0 0
1
1 1 1 1 0
OP
DR
SR
imm5
15
12
11
9
8
6
0
5
4
Register file
SR
DR
From FSM
Instruction register
Sign-extend

## Slide 23: Instructions with one Literal in MIPS
I-type
  2 register operands and immediate
Some operate and data movement instructions
  opcode = operation
  rs = source register
  rt =
    destination register in some instructions (e.g., addi, lw)
    source register in others (e.g., sw)
  imm = Literal or immediate
opcode
rs
rt
imm
6 bits
5 bits
5 bits
16 bits

## Slide 24: Add with one Literal in MIPS
Add immediate
0
17
16
5
op
rs
rt
imm
addi $s0, $s1, 5
MIPS assembly
Field Values
001000
10001
10010
0000 0000 0000 0101
op
rs
rt
imm
Machine Code
0x22300005
      rt ← rs + sign-extend(imm)

## Slide 25: Subtract in LC-3
MIPS assembly
LC-3 assembly
Tradeoff in LC-3
  More instructions
  But, simpler control logic
a = b + c - d;
add $t0, $s0, $s1
sub $s3, $t0, $s2
High-level code
MIPS assembly
a = b + c - d;
ADD R2, R0, R1
NOT R4, R3
ADD R5, R4, #1
ADD R6, R2, R5
High-level code
LC-3 assembly
2’s complement of R3
Notes: In LC-3 we would need to calculate 2’s complement of d

## Slide 26: Subtract Immediate
MIPS assembly
LC-3
a = b - 3;
subi $s1, $s0, 3
High-level code
MIPS assembly
Is subi necessary in MIPS?
addi $s1, $s0, -3
MIPS assembly
a = b - 3;
ADD R1, R0, #-3
High-level code
LC-3 assembly
Notes: Negative immediate is 2’s complement

## Slide 27: Data Movement Instructions and Addressing Modes

## Slide 28: Data Movement Instructions
In LC-3, there are seven data movement instructions
  LD, LDR, LDI, LEA, ST, STR, STI
Format of load and store instructions
  Opcode (bits [15:12])
  DR or SR (bits [11:9])
  Address generation bits (bits [8:0])
  Four ways to interpret bits, called addressing modes
    PC-Relative Mode
    Indirect Mode
    Base+offset Mode
    Immediate Mode
In MIPS, there are only Base+offset and immediate modes for load and store instructions
Notes: x86-64 addressing modes:
movl $1, 0x604892 # direct (address is constant value)
movl $1, (%rax) # indirect (address is in register %rax)
movl $1, -24(%rbp) # indirect with displacement
(address = base %rbp + displacement -24)
movl $1, 8(%rsp, %rdi, 4) # indirect with displacement and scaled-index
(address = base %rsp + displ 8 + index %rdi * scale 4)
movl $1, (%rax, %rcx, 8) # (special case scaled-index, displ assumed 0)
movl $1, 0x8(, %rdx, 4) # (special case scaled-index, base assumed 0)
movl $1, 0x4(%rax, %rcx) # (special case scaled-index, scale assumed 1)

## Slide 29: PC-Relative Addressing Mode
LD (Load) and ST (Store)
  OP = opcode
    E.g., LD = 0010
    E.g., ST = 0011
  DR = destination register in LD
  SR = source register in ST
  LD: DR ← Memory[PC✝ + sign-extend(PCoffset9)]
  ST: Memory[PC✝ + sign-extend(PCoffset9)] ← SR
OP
DR/SR
PCoffset9
4 bits
3 bits
9 bits
15
14
13
12
11
10
9
8
7
6
2
1
0
5
4
3
      ✝This is the incremented PC

## Slide 30: LD in LC-3
LD assembly and machine code
LD R2, 0x1AF
LC-3 assembly
Field Values
Machine Code
2
2
0x1AF
OP
DR
PCoffset9
0 0 1 0
0 1 0
1 1 0 1 0 1 1 1 1
OP
DR
PCoffset9
15
12
11
9
8
0
Register file
DR
Instruction register
Sign-extend
Incremented PC
1. Address calculation
2. Memory read
3. DR is loaded
The memory address is only +255 to -256 locations away of the LD or ST instruction
Limitation: The PC-relative addressing mode cannot address far away from the instruction

## Slide 31: Indirect Addressing Mode
LDI (Load Indirect) and STI (Store Indirect)
  OP = opcode
    E.g., LDI = 1010
    E.g., STI = 1011
  DR = destination register in LDI
  SR = source register in STI
  LDI: DR ← Memory[Memory[PC✝ + sign-extend(PCoffset9)]]
  STI: Memory[Memory[PC✝ + sign-extend(PCoffset9)]] ← SR
OP
DR/SR
PCoffset9
4 bits
3 bits
9 bits
15
14
13
12
11
10
9
8
7
6
2
1
0
5
4
3
      ✝This is the incremented PC

## Slide 32: LDI in LC-3
LDI assembly and machine code
LDI R3, 0x1CC
LC-3 assembly
Field Values
Machine Code
A
3
0x1CC
OP
DR
PCoffset9
1 0 1 0
0 1 1
1 1 1 0 0 1 1 0 0
OP
DR
PCoffset9
15
12
11
9
8
0
Now the address of the operand can be anywhere in the memory
Register file
DR
Instruction register
Sign-extend
Incremented PC
1. Address calculation
2. Memory read
5. DR is loaded
4. Memory read
3. Loaded address from MDR to MAR

## Slide 33: Base+Offset Addressing Mode
LDR (Load Register) and STR (Store Register)
  OP = opcode
    E.g., LDR = 0110
    E.g., STR = 0111
  DR = destination register in LDR
  SR = source register in STR
  LDR: DR ← Memory[BaseR + sign-extend(offset6)]
  STR: Memory[BaseR + sign-extend(offset6)] ← SR
OP
DR/SR
offset6
4 bits
3 bits
6 bits
15
14
13
12
11
10
9
8
7
6
2
1
0
5
4
3
BaseR
3 bits

## Slide 34: LDR in LC-3
LDR assembly and machine code
LDR R1, R2, 0x1D
LC-3 assembly
Again, the address of the operand can be anywhere in the memory
1. Address calculation
2. Memory read
3. DR is loaded
Field Values
6
1
0x1D
OP
DR
offset6
2
BaseR
Machine Code
0 1 1 0
0 0 1
0 1 1 1 0 1
OP
DR
offset6
15
12
11
9
8
0
0 1 0
BaseR
6
5
Register file
DR
Instruction register
Sign-extend
BaseR
001
010
0110
Notes: Errata in Figure 5.8 in DR and BaseR

## Slide 35: Base+Offset Addressing Mode in MIPS
In MIPS, lw and sw use base+offset mode (or base addressing mode)
imm is the 16-bit offset, which is sign-extended to 32 bits
A[2] = a;
sw $s3, 8($s0)
High-level code
MIPS assembly
Memory[$s0 + 8] ← $s3
43
16
19
8
op
rs
rt
imm
Field Values

## Slide 36: An Example Program in MIPS and LC-3
a = A[0];
c = a + b - 5;
B[0] = c;
A = $s0
b = $s2
B = $s1
High-level code
MIPS registers
LDR R5, R0, #0
ADD R6, R5, R2
ADD R7, R6, #-5
STR R7, R1, #0
LC-3 assembly
lw $t0, 0($s0)
add $t1, $t0, $s2
addi $t2, $t1, -5
sw $t2, 0($s1)
MIPS assembly
A = R0
b = R2
B = R1
LC-3 registers

## Slide 37: Immediate Addressing Mode
LEA (Load Effective Address)
  OP = 1110
  DR = destination register
  LEA: DR ← PC✝ + sign-extend(PCoffset9)
OP
DR
PCoffset9
4 bits
3 bits
9 bits
15
14
13
12
11
10
9
8
7
6
2
1
0
5
4
3
      ✝This is the incremented PC
What is the difference from PC-Relative addressing mode?
Answer: Instructions with PC-Relative mode access memory,
but LEA does not  Hence the name Load Effective Address

## Slide 38: LEA in LC-3
LEA assembly and machine code
LEA R5, #-3
LC-3 assembly
Field Values
Machine Code
E
5
0x1FD
OP
DR
PCoffset9
1 1 1 0
1 0 1
1 1 1 1 1 1 1 0 1
OP
DR
PCoffset9
15
12
11
9
8
0
Register file
DR
Instruction register
Sign-extend
Incremented PC

## Slide 39: Immediate Addressing Mode in MIPS
In MIPS, lui (load upper immediate) loads a 16-bit immediate into the upper half of a register and sets the lower half to 0
It is used to assign 32-bit constants to a register
a = 0x6d5e4f3c;
# $s0 = a
lui $s0, 0x6d5e
ori $s0, 0x4f3c
High-level code
MIPS assembly

## Slide 40: Addressing Example in LC-3
What is the final value of R3?
x30F4
P&P, Chapter 5.3.5
Notes: Erratum in Figure 5.10 in x30F4

## Slide 41: Addressing Example in LC-3
What is the final value of R3?
The final value of R3 is 5
x30F4
LEA
ADD
ST
AND
ADD
STR
LDI
-3
14
-5
5
14
-9
0
R3 = M[M[PC – 9]] = M[M[0x30FD – 9]] =
R1 = PC – 3 = 0x30F7 – 3 = 0x30F4
R2 = R1 + 14 = 0x30F4 + 14 = 0x3102
M[PC - 5] = M[0x030F4] = 0x3102
R2 = 0
R2 = R2 + 5 = 5
M[R1 + 14] = M[0x30F4 + 14] = M[0x3102] = 5
M[M[0x30F4]] = M[0x3102] = 5
P&P, Chapter 5.3.5
Notes: Optional example

## Slide 42: Control Flow Instructions

## Slide 43: Control Flow Instructions
Allow a program to execute out of sequence
Conditional branches and jumps
  Conditional branches are used to make decisions
    E.g., if-else statement
  In LC-3, three condition codes are used
  Jumps are used to implement
    Loops
    Function calls
  JMP in LC-3 and j in MIPS

## Slide 44: Condition Codes in LC-3
Each time one GPR (R0-R7) is written, three single-bit registers are updated
Each of these condition codes are either set (set to 1) or cleared (set to 0)
  If the written value is negative
    N is set, Z and P are cleared
  If the written value is zero
    Z is set, N and P are cleared
  If the written value is positive
    P is set, N and Z are cleared
x86 and SPARC are examples of ISAs that use condition codes

## Slide 45: Conditional Branches in LC-3
BRz (Branch if Zero)
  n, z, p = which condition code is tested (N, Z, and/or P)
    n, z, p: instruction bits to identify the condition codes to be tested
    N, Z, P: values of the corresponding condition codes
  PCoffset9 = immediate or constant value
  if ((n AND N) OR (p AND P) OR (z AND Z))
    then PC ← PC✝ + sign-extend(PCoffset9)
  Variations: BRn, BRz, BRp, BRzp, BRnp, BRnz, BRnzp
BRz PCoffset9
0000
n
PCoffset9
4 bits
9 bits
z
p
      ✝This is the incremented PC

## Slide 46: Conditional Branches in LC-3
BRz
BRz 0x0D9
What if n = z = p = 1?*
(i.e., BRnzp)
And what if n = z = p = 0?
Instruction register
Program Counter
Condition registers
n z p
      *n, z, p are the instruction bits to identify the condition codes to be tested

## Slide 47: Conditional Branches in MIPS
beq (Branch if Equal)
  4 = opcode
  rs, rt = source registers
  offset = immediate or constant value
  if rs == rt
    then PC ← PC✝ + sign-extend(offset) * 4
  Variations: beq, bne, blez, bgtz
4
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
beq $s0, $s1, offset
      ✝This is the incremented PC

## Slide 48: Branch If Equal in MIPS and LC-3
This is an example of tradeoff in the instruction set
  The same functionality requires more instructions in LC-3
  But, the control logic requires more complexity in MIPS
beq $s0, $s1, offset
LC-3 assembly
MIPS assembly
NOT R2, R1
ADD R3, R2, #1
ADD R4, R3, R0
BRz offset
Subtract (R0 - R1)

## Slide 49: Lecture Summary
Instruction Set Architectures: LC-3 and MIPS
  Operate instructions
  Data movement instructions
  Control instructions
Instruction formats
Addressing modes

## Slide 50: Digital Design & Computer Arch. Lecture 10a: Instruction Set Architecture
Prof. Onur Mutlu
ETH Zürich
Spring 2020
20 March 2020